## Slide 1: Eddy-Covariance Fundamentals
From: Gough, C. M., Giffen, C., Woodward, T. W. (2018). Environmental Drivers of Ecosystem Carbon Fluxes from Minutes to Years. NEON Faculty Mentoring Network, QUBES Educational Resources. doi:10.25334/Q4VD7W
Images: C. Gough

## Slide 2: NEON Education video: “Eddy Covariance: Measuring an Ecosystem's Breath”
https://youtu.be/CR4Anc8Mkas
Notes: This NEON Science video

## Slide 3
Global Carbon Project
Le Quéré et al. 2017
Global Carbon Budget
Pg C yr-1
44%
28%
22%

## Slide 4: The challenge: estimating ecosystem-scale carbon fluxes at high temporal resolution
Net ecosystem production =
Gross primary production – Ecosystem respiration,
Usually expressed as annual rate
Net ecosystem CO2 exchange =
Same as above, but usually expressed as instantaneous rate

## Slide 5
CO2
Roots
Leaves
Heterotrophic
respiration
Dead wood
Net ecosystem production = Net primary production – Heterotrophic respiration
Live wood
Inventory method
Images: C. Gough and P. Curtis

## Slide 6: Advances in early 90’s set stage for broad use of eddy-covariance
Instrumentation: IRGA and wind speed sensors (anemometers).
Data analysis and storage: Computer processing and hard drive space
Methodological development: Developed from fluid dynamics, meteorological, and engineering principles
Old IRGAs were the size of refrigerators
Images: Wikipedia

## Slide 7: First paper on eddy-covariance 25 years ago from Harvard Forest

## Slide 8
Eddy-covariance theory
Artist: Catherine McGuigan, VCU BS ‘18
Notes: For a primer of eddy-covariance see box 1 of: https://nph.onlinelibrary.wiley.com/doi/10.1111/nph.15227 and https://en.wikipedia.org/wiki/Eddy_covariance

## Slide 9: Flux (F) derived from eddy-covariance
Fluctuation of [CO2] from mean
(g kg air-1)
Density of air
(kg air m-3)
Velocity of air moved upward or downward (m s-1)
The covariance is calculated between the fluctuating component of the vertical wind and the fluctuating component of gas concentration.
Source: Burba, G., 2013. Eddy Covariance Method for Scientific, Industrial, Agricultural, and Regulatory Applications: A Field Book on Measuring Ecosystem Gas Exchange and Areal Emission Rates. LI-COR Biosciences, Lincoln, NE, USA, 331 pp.

## Slide 10: Eddy-covariance instrumentation
3-D Sonic Anemometer
Air intake to IRGA (closed path)
Thermocouple and other climate sensors
Open path IRGA
Images: C. Gough and C. Vogel; and http://www.ese.u-psud.fr/IMG/jpg/Li-7500ter-2.jpg

## Slide 11
Image: C. Gough
Notes: Eddy-covariance tower in a temperate forest ecosystem

## Slide 12: Terrestrial Observation System (TOS)
Image: NEON
Notes: Eddy-covariance tower in the Central US plains

## Slide 13
Image: C. Gough
Notes: Eddy-covariance tower in a tidal wetland

## Slide 15: Methodological strengths
Medium-spatial scale resolution (1 km2)
Integrates multiple flux sources
Very high temporal resolution (1/2 hour)
Relatively high accuracy
Source: NASA

## Slide 16: Methodological limitations
Flux “footprint” size and location varies over time
Must have wind!
Not amenable to complex terrain
Does not tell you where carbon (or other trace gases) go once they enter the ecosystem
Remains computationally intensive
Credit: Gil Bohrer
Notes: The figure above shows the footprint probability, with, for example, “80” indicating that 80 % of the carbon fluxes originate within the mapped area.

## Slide 17
Total daytime uptake: 98.9 mmol CO2 m-2
Total nighttime loss: 57.3 mmol CO2 m-2
Net 24 hour gain: 41.6 mmol CO2 m-2
or, 5.0 kg C ha-1 (27 lbs C per acre)
Total daytime uptake: 7,402 kg C ha-1
Total nighttime loss: 6,599 kg C ha-1
Net annual gain: 803 kg C ha-1
(2.2 short tons C per acre)
Notes: Instantaneous rates (y-axis) are in micromoles. When summed over the course of a day, the quantity amounts to millimoles.

## Slide 18
Towers measure Net Ecosystem Productivity
Net Ecosystem Productivity =
Photosynthesis – Respiration
or
NEP = GPP – Re

## Slide 19
Nighttime =
no photosynthesis =
- Re
Daytime =
Photosynthesis – Respiration =
GPP - Re
We can use the nighttime measurements to determine Re and remove Re from NEP in the day to get GPP
Notes: Instantaneous rates (y-axis) are in micromoles. When summed over the course of a day, the quantity amounts to millimoles.

## Slide 20: The value of observational networks A proliferation of eddy-covariance towers is enabling understanding of ecosystem carbon fluxes worldwide.
Credit: https://fluxnet.fluxdata.org/about/
Credit: Whittaker, 1975
We might expect that climate variability affects carbon fluxes, making a global network of eddy-covariance towers critical to understanding how different ecosystems in different climate zones cycle carbon.